## Slide 1: GEM Minidrift detector with chevron Readout
EIC Tracking Meeting 10/6/14
B.Azmoun, BNL

## Slide 2: Align mini-drift and Ref. detector
Alignment is achieved by scanning Si alignment parameters to minimize resolution
(f, DZ, (q x, q y), (Dx, Dy)
GEM
Minidrift
Si Telescope
120GeV/c beam
Set Up
x
y
z
f
q
GEM
Minidrift Det.
Si Ref. Telescope
12”
Particle Beam
(π+, +120GeV/c)
Resolution measured as a function of theta, for three different phi orientations (0, 45, and 90 degrees)
Si Tel
Minidrift

## Slide 3: Example: Phi Scan, theta_x,y Scan

## Slide 4: Vector Reco. Methods Investigated
1. Charge Projection: Use projection of charge cloud on pad plane to reconstruct vector angle. The vector position on the pad plane is determined by the earliest pad hit.
Leads to discrete values for vector position, determined by strip segmentation Poor Quality
Strips
Vertical Extent of Vector
defined by Drift Gap width
Horizontal Extent of Vector defined by charge projection
2. Charge-Centroid for each Time bin:
A charge weighted position centroid is calc. for each time bin of all strips, which gives the vector position on the pad plane at each time bin.
The time bin value, then gives a measure of the charge arrival time, which may be translated into a z-coord. using the drift velocity.
Thus, for each time bin, an (x,y) point along the track is determined. The resulting array of points is then fit to straight line to reconstruct the track.
 Requires careful treatment of the baseline noise to avoid incorporating noise into analysis.
Raw Data: Waveforms in Time
3. Use Charge arrival time to calculate z-coord:
Exploit timing info. by fitting rising edge of the waveform from each strip to a straight line to determine the time axis intercept, which gives a measure of the charge arrival time for that strip.
The center 0f the strip may then be taken as the position of the track at that time.
 Most promising Results when
Not so good
Limited by low charge sharing on COMPASS Strip Readout
Great for Chevron Readout! (Chevrons are naturally amenable to centroid calc./ relatively high charge sharing)
Great for COMPASS Strip Readout (many strips hit)
Limited by number of strips hit for Chevron Readout

## Slide 5: Some Event Displays for time bin centroid method
Though there a relatively few pads hit in this event, the vector fit still has a good number of points to fit to since there is a point for every time bin.
Precise timing info is traded for accurate timing info (40MHz ADC clock) and the centroid calc. using 2mm chevron pads approaches or is better than the resolution of single 400um strip.

## Slide 6: CENTROID Calc.
Centroid spikes correspond to single pad events (want to avoid these by either using gas with higher transverse diffusion or increase diffusion by increasing induction gap, etc)
The 2D scatter plot of the residual per event as a function of the measured centroid allows one to establish an error function to be used to correct the measured centroid.
The error function is (more or less) single valued as a function of the measured centroid, allowing one to calibrate the readout board in the lab (or at zero deg.) for use in a beam test.
At 30 deg. the error function smears out since many pads are hit, thus many points along the zigzag structure are sampled, leading to a multi-valued (smeared out) error function that averages to zero.
Zero Degrees
30 Degrees

## Slide 7: Vector Reco (zero degrees)
Vector reco at small angles using this method is quite impressive. Despite the fact that only two or three pads are hit per event, the vector fit has an (x,z) pair from each time bin used to measure the centroid (10 – 20 points).
Centroid spikes are still apparent, likely from 2 or three pad events with poor charge sharing (ie the vast majority of the charge is on a single pad).
Error function works pretty well.

## Slide 8: Vector Reco (30 degrees)
No spikes in vect. position distribution
Again, since the 2d scatter plot of the residual Vs the calculated vector position is multi-valued, it averages to zero and is useless.
However, if we use the measured error function at zero degrees, and it apply to each centroid calculation of each time bin, a true error correction may then be recuperated  work in progress

## Slide 9: Compare Resolution
Vect. Reco: | Fitting Rising edge of Pulse | Res. | ~300um | 
Vect Reco: | Centroid per Time bin (Full Pulse width) |  |  | 
 |  | RESOLUTION |  | 
Angle (deg) |  | Centroid (um) | Vect Reco. (um) | Weighted (um)
0 | Uncorrected Res. | 140.87 | 151.58 | 140.04
0 | Corrected Res. | 85.13 | 92.85 | 80.62
30 | Uncorrected Res. | 893.78 | 231.13 | 
30 | Corrected Res. | 937.86 | 230.4 | 
Vect Reco: | Centroid per Time bin (Truncated Pulse width) |  |  | 
30 | Uncorrected Res. |  | 207.5 | 208.3
30 | Corrected Res. |  | 203.14 | 202.3
Compare resolution from three vector
Reco methods
Tradiotnal vector reco: fit rising edge of pulse
to line to get time intercept
 Used for COMPASS readout board and gave good results since many pads were hit and the charge sharing didn’t need to be very high
Time bin centroid method: requires good charge sharing, but not too many pads need
to be hit per event.
Time bin centroid with PA Pulse truncation: Due to the rather slow falling edge of the PA response function, the amplitude of this tail doesn’t accurately represent charge that is in the detector, so we must truncate the pulse shape. This is a balancing act since some charge does in fact arrive later in time amount of truncation must be optimized (done!)

## Slide 10: Conclusions
With the use of this new time bin centroid method, the resolution obtained using the chevron pads is comparable with the method used in analyzing the data from the COMPASS readout, all the while recruiting 4 to 5 times fewer hit pads to get the job done.
This method is amenable with the use of the following tricks
  Weighted vector reco
  Correction function (point by point)
  PA pulse truncation optimization
  Can we incorporate the traditional and new method into a hybrid method to get a better result still? For instance, weight the centroid and the two vector reco methods to find the position.